## Slide 1: 5XTA0 - Computer Networks
Exam Questions Bank
Link layer routing, IP Addresses, CIDR

## Slide 2: Question 2 Description
The figure below illustrates three terminal nodes connected via a network of 5 IP routers and one link-layer hub. The distance of the link between two Ethernet ports is indicated with a number. No router has a default gateway. The IP address of each port is given in the table below the figure. Answer the following questions.

## Slide 3: Question 2 Description

## Slide 4: Question 2.A
Assume terminal B just joined the 10.0.8.4/30 network and has no entries in the routing table. Terminal B wants to send an IP packet to A and C but is not aware of the MAC address of either of them. Provide the sequence of messages generated in the network before the IP packet from B to A and C can be delivered. Use IP or physical addresses as needed and payload if known in the format below.
B to A
1. Protocol: ARP From:_B_______ To:__all________ Payload:
  HW Address of B.eth0, IP Addr of B (10.0.8.6), HW addr of A.eth0 (not known), IP Addr of A (10.0.8.5)
2. Protocol: ARP From:_A_________ To:_B________ Payload:
  HW addr of A.eth0, IP Addr of A (10.0.8.5), HW Address of B.eth0, IP Addr of B (10.0.8.6)
3. Protocol:_IP___ From:_10.0.8.6_ To:_10.0.8.5_ Payload: data
B to C
1. Protocol: ARP From:_B_______ To:__all________ Payload:
  HW Address of B.eth0, IP Addr of B (10.0.8.6), HW addr of C.eth0 (not known), IP Addr of C (192.168.87.31)
2. Protocol: ARP From:_R1_________ To:_B________ Payload:
  HW addr of R1.eth2, IP Addr of R1 (10.0.8.7), HW Address of B.eth0, IP Addr of B (10.0.8.6)
3. Protocol:_IP___ From:_10.0.8.6_ To:_10.0.8.7_ Payload: data

## Slide 5: Question 2.B
Assume terminal B just joined the 10.0.8.4/30 network and has no entries in the routing table. Terminal B wants to send an IP packet to C. Provide the minimal routing table of B which would allow the packet to be routed to C.

## Slide 6: Question 2.C
Build the routing table of R1. Consider all the possible L3 routes. Use CIDR where possible.
Prefix | Mask | Device (port)
10.0.8.4 64.155.12.105 0.0.0.0 64.155.92.61 64.155.41.89 64.155.12.106 64.155.31.13 64.155.32.67 192.168.87.31 64.155.50.1 64.155.50.2 192.168.87.39 64.155.41.90 64.155.92.62 64.155.42.35 64.155.32.66 64.155.42.34 64.155.31.12 | /30 /32 /0 | eth2 eth1 eth0

## Slide 7: Question 2.C
Build the routing table of R1. Consider all the possible L3 routes. Use CIDR where possible.
Prefix | Mask | Device (port)
10.0.8.4 64.155.12.105 0.0.0.0 | /30 /32 /0 | eth2 Eth1 eth0

## Slide 8: Question 2.C
Build the routing table of R5. Consider all the possible L3 routes. Use CIDR where possible.
Prefix | Mask | Device (port)
10.0.8.4 192.168.87.0 64.155.41.64 64.155.92.60 64.155.32.64 64.155.31.0 64.155.42.34 64.155.42.32 64.155.50.1 64.155.50.0 64.155.12.105 64.155.12.104 | /30 /24 /26 /30 /25 /25 /32 /30 /32 /30 /32 /30 | eth1 eth0 eth1 eth1 eth0 eth0 eth2 eth0 eth1 eth0 eth1 eth0

## Slide 9: Question 2.C
Build the routing table of R5. Consider all the possible L3 routes. Use CIDR where possible.
Prefix | Mask | Device (port)
10.0.8.4 192.168.87.0 64.155.41.64 (41=00101001) 64.155.92.60 (92=01011100) -> 64.155.41.0 -> 64.155.92.0 64.155.32.64 64.155.31.0 64.155.42.34 64.155.42.32 64.155.50.1 64.155.50.0 64.155.12.105 64.155.12.104 -> 0.0.0.0 | /30 /24 /26 /30 -> /24 -> /24 /25 /25 /32 /30 /32 /30 /32 /30 /0 | eth1 eth0 eth1 eth1 -> eth1 -> eth1 eth0 eth0 eth2 eth0 eth1 eth0 eth1 eth0 eth0

## Slide 10: Question 2.C
Build the routing table of R5. Consider all the possible L3 routes. Use CIDR where possible.
Prefix | Mask | Device (port)
10.0.8.4 192.168.87.0 64.155.41.0 64.155.92.0 64.155.42.34 64.155.50.1 64.155.12.105 0.0.0.0 | /30 /24 /24 /24 /32 /32 /32 /0 | eth1 eth0 eth1 eth1 eth2 eth1 eth1 eth0